Chapter 296-809 WAC

Safety Standards for Confined Spaces

WAC 296-809-099  Definitions.	1

WAC 296-809-100 Scope.	9

WAC 296-809-200  Identifying and controlling permit-required confined spaces.	11

WAC 296-809-20002  Identify permit-required confined spaces.	11

WAC 296-809-20004  Inform employees and control entry to permit-required confined spaces.	13

WAC 296-809-20006  Follow these requirements when you contract with another employer to enter your confined space.	13

WAC 296-809-300  Permit-required confined space program.	15

WAC 296-809-30002  Develop a written permit-required confined space program.	15

WAC 296-809-30004  Meet these additional requirements if your employees enter another employer's confined space.	17

WAC 296-809-400  Employee Training.	18

WAC 296-809-40002  Provide employee training.	18

WAC 296-809-40004  Certify employee proficiency.	20

WAC 296-809-500  Permit-entry procedures.	21

WAC 296-809-50002  Implement procedures for entry permits.	21

WAC 296-809-50004  Use an entry permit that contains all required information.	22

WAC 296-809-50006  Keep and review your entry permits.	23

WAC 296-809-50008  Prevent unauthorized entry.	24

WAC 296-809-50010  Provide, maintain, and use proper equipment.	24

WAC 296-809-50012  Evaluate and control hazards for safe entry.	25

WAC 296-809-50014  Make sure you have adequate rescue and emergency services available.	27

WAC 296-809-50016  Use nonentry rescue systems or methods whenever possible.	28

WAC 296-809-50018  Make sure entry supervisors perform their responsibilities and duties.	29

WAC 296-809-50020  Provide an attendant outside the permit-required confined space.	30

WAC 296-809-50022  Make sure entrants know the hazardous conditions and their duties.	32

WAC 296-809-50024  Implement procedures for ending entry.	32

WAC 296-809-600  Alternate entry procedures.	33

WAC 296-809-60002  Make sure the following conditions are met if using alternate entry procedures.	33

WAC 296-809-60004  Follow these alternate entry procedures for permit-required confined spaces.	34

WAC 296-809-700  Nonpermit confined spaces requirements.	36

WAC 296-809-70002  Follow these requirements when classifying a confined space as a nonpermit confined space.	37

WAC 296-809-70004  Reevaluate nonpermit confined spaces if hazards develop.	38

WAC 296-809-099  Definitions.

Acceptable entry conditions.  The conditions that must exist in a permit-required confined space to allow safe entry and work.

Attendant.  An individual stationed outside one or more permit-required confined spaces to monitor the entrants.  Attendants must perform the duties required in WAC 296-809-50020.

Blanking or blinding.  The absolute closure of a pipe, line, or duct by fastening a solid plate (such as a spectacle blind or a skillet blind) that completely covers the bore.  It is capable of withstanding the maximum pressure of the pipe, line, or duct with no leakage beyond the plate.

Competent person. One who is capable of identifying existing and predictable hazards in the surroundings or working conditions which are unsanitary, hazardous, or dangerous to employees, and who has the authorization to take prompt corrective measures to eliminate them. They shall be knowledgeable in this chapter.

Confined space.  A space that is all of the following:

Large enough and arranged so an employee could fully enter the space and work.

Has limited or restricted entry or exit.  Examples of spaces with limited or restricted entry are tanks, vessels, silos, storage bins, hoppers, vaults, excavations, and pits.

Not primarily designed for continuous human occupancy.

Note: See Appendix A in the Resource Section for examples of Confined Spaces

Control.  The action taken to reduce the level of any hazard inside a confined space using engineering methods (for example, ventilation), and then using these methods effectively to maintain the reduced hazard level.  Control also refers to the engineering methods used for this purpose.  Personal protective equipment is not a control.

Controlling Contractor (employer).   The employer that has overall responsibility for construction at the worksite. If the controlling contractor (employer) owns or manages the property, then it is both a controlling employer and a host employer.

Double block and bleed.  The closure of a line, duct, or pipe by closing and locking or tagging 2 in-line valves and by opening and locking or tagging a drain or vent valve in the line between the 2 closed valves.

Early-warning system.  The method used to alert authorized entrants and attendants that an engulfment hazard may be developing. Examples of early-warning systems include:  alarms activated by remote sensors; and lookouts with equipment for immediately communicating with the authorized entrants and attendants.

Eliminate–nated (Webster’s II New College Dictionary) to get rid of.  Remove – to eliminate a hazard.

Emergency.  Any occurrence (including any failure of hazard control or monitoring equipment) or event internal or external to the permit-required confined space that could endanger authorized entrants.Engulfment.  The surrounding and effective capture of a person by a liquid or finely divided (flowable) solid substance that can be inhaled to cause death by filling or plugging the respiratory system or that can exert enough force on the body to cause death by strangulation, constriction, or crushing.

Enter (entry).  The action by which a person passes through an opening into a permit-required confined space and includes work activities in that space.  Entry is considered to have occurred as soon as any part of the entrant's body breaks the plane of an opening into the space. Entry includes ensuing work activities in that space and is considered to have occurred as soon as any part of the entrant’s body breaks the plane of an opening into the space, whether or not such action is intentional or any work activities are actually performed in the space.

Entrant.  An employee who is authorized by the employer to enter a permit-required confined space.

Entry Employer. Any employer who has an employee  enter a permit space.

Note: An employer cannot avoid the duties of the standard merely by refusing to decide whether its employees will enter a permit space, and OSHA will consider the failure to so decide to be an implicit decision to allow employees to enter those spaces if they are working in the proximity of the space.

Entry permit (permit).  The written or printed document that is provided by you to allow and control entry into a permit-required confined space and that contains the information required in WAC 296-809-500, Permit entry procedures.

Entry rescue.   Occurs when a rescue service enters a permit space to rescue one or more employees.

Entry supervisor.  The qualified person (such as the employer, crew leader, or crew chief) responsible for:

(a) Determining if acceptable entry conditions are present at a permit-required confined space where entry is planned;

(b) Authorizing entry and overseeing entry operations; and

(c) Terminating entry as required by this standard.

Note. An entry supervisor also may serve as an attendant or as an authorized entrant, as long as that person is trained and equipped as required by this standard for each role he or she fills. Also, the duties of entry supervisor may be passed from one individual to another during the course of an entry operation.

Hazardous atmosphere.  An atmosphere that may expose employees to the risk of death, incapacitation, impairment of ability to self-rescue (that is, escape unaided from a permit-required confined space), injury, or acute illness caused by one or more of the following:

(a) Flammable gas, vapor, or mist in excess of 10 percent of its lower flammable limit (LFL).

(b) Airborne combustible dust at a concentration that meets or exceeds its LFL. The concentration may be approximated as a condition in which the dust obscures vision at a distance of 5 feet (1.52m) or less.

(c) Atmospheric oxygen concentration below 19.5 percent or above 23.5 percent.

Atmospheric concentration of any substance which may exceed a permissible exposure limit.  For additional information about atmospheric concentration, see chapter 296-62 WAC, Parts F, G, and I, General occupational health standards and chapter 296-841 WAC, Airborne contaminants.1

Any other atmospheric condition that is immediately dangerous to life or health.

1 Note: An airborne concentration of a substance that is not capable of causing death, incapacitation, impairment of ability to self-rescue, injury, or acute illness due to its health effects is not covered by this definition.

Note: You can find guidance on establishing acceptable atmospheric conditions for air contaminants, which have no WISHA-determined doses or permissible exposure limits using other sources of information, such as: Safety data sheets required by WAC 296-901-14014, Safety data sheets. Published information. Internal documents.

Hot work.  Operations capable of providing a source of ignition (for example, riveting, welding, cutting, burning, and heating).

Hot work permit.  A written authorization to perform operations, for example, riveting, welding, cutting, burning, and heating, that can provide a source of ignition.

Host employer.  The employer that owns or manages the property where the work is taking place.  In no case with there be more than one host employer.

Note. If the owner of the property on which the construction activity occurs has contracted in writing with an entity for the general management of that property, and has in writing transferred to that entity the information specified in WAC 296-809-20006. OSHA will treat the contracted management entity as the host employer for as long as that entity manages the property. Otherwise, OSHA will treat the owner of the property as the host employer.

Immediately dangerous to life or health (IDLH)  Any of the following conditions:

(a)  An immediate or delayed threat to life.

(b) Anything that would cause irreversible adverse health effects.

(c) Anything that would interfere with an individual's ability to escape unaided from a permit-required confined space.

Note: Some materials - hydrogen fluoride gas and cadmium vapor, for example - may produce immediate transient effects that, even if severe, may pass without medical attention, but are followed by sudden, possibly fatal collapse 12 to 72 hours after exposure. The victim “feels normal” after recovery from transient effects until collapse. Such materials in hazardous quantities are considered to be “immediately” dangerous to life or health (IDLH).

Inerting.  The displacement of the atmosphere in a permit-required confined space by a noncombustible gas (such as nitrogen) to such an extent that the resulting atmosphere is noncombustible.  This procedure produces an IDLH oxygen-deficient atmosphere.

.

Isolation.  The process by which a permit-required confined space is removed from service and completely protected against the release of energy and material into the space by such means as:  Blanking or blinding; misaligning or removing sections of lines, pipes, or ducts; a double block and bleed system; lockout or tagout of all sources of energy; or blocking or disconnecting all mechanical linkages or placement of barriers to eliminate the potential for employee contact with a physical hazard.  See Appendix A.

Limited or restricted means of entry or exit.   A condition that has a potential to impede an employee’s movement into or out of a confined space.  Such conditions include, but are not limited to, trip hazards, poor illumination, slippery floors, inclining surfaces and ladders.

A space has limited or restricted means of entry or exit, if an entrant’s ability to escape in an emergency would be hindered.

Line breaking.  The intentional opening of a pipe, line, or duct that is or has been carrying flammable, corrosive, or toxic material, an inert gas, or any fluid at a volume, pressure, or temperature capable of causing injury.

Lockout.  Placing a lockout device on an energy-isolating device using an established procedure to make sure the machine or equipment cannot be operated until the lockout device is removed. For more information see Chapter 296-803 WAC Control of Hazardous Energy.

Lockout device.  A device that uses a positive means, such as a key or combination lock, to hold an energy-isolating device in the “safe” or “off” position. This includes blank flanges and bolted slip blinds.

Lower flammable limit or lower explosive limit.  The minimum concentration of a substance in air needed for an ignition source to cause a flame or explosion.

Monitor or monitoring.  The process used to identify and evaluate the hazards after an authorized entrant enters the space. This is a process of checking for changes that is performed in a periodic or continuous manner after the completion of the initial testing or evaluation of that space.

Non-entry rescue.   Occurs when a rescue service, usually the attendant, retrieves employees in a permit space without entering the permit space.

Nonpermit confined space.  A confined space that does not contain actual hazards or potential hazards capable of causing death or serious physical harm.

Oxygen deficient atmosphere.  An atmosphere containing less than 19.5 percent oxygen by volume.

Oxygen enriched atmosphere.  An atmosphere containing more than 23.5 percent oxygen by volume

Permit-required confined space or permit space.  A confined space that has one or more of the following characteristics capable of causing death or serious physical harm:

- Contains or has a potential to contain a hazardous atmosphere.

- Contains a material with the potential for engulfing someone who enters.

- Has an internal configuration that could allow someone entering to be trapped or asphyxiated by inwardly converging walls or by a floor, which slopes downward and tapers to a smaller cross section.

- Contains any physical hazard.  This includes any recognized health or safety hazards including engulfment in solid or liquid material, electrical shock, or moving parts.

(e) Contains any other recognized serious safety or health hazard that could either:

(i)	Impair the ability to self-rescue; or

(ii)	Result in a situation that presents an immediate danger to life or health.

See Appendix B for examples of Permit-Required Confined Space Hazards.

Permit-required confined space program.  An overall program for:

(a) Controlling and appropriately protecting employees from permit-required confined space hazards; and

(b) Regulating employee entry into permit-required confined spaces.

Physical hazard.  An existing or potential hazard that can cause death or serious physical damage. Examples include, but are not limited to: explosives (as defined by WAC 296-52- 60130); mechanical, electrical, hydraulic energy, pneumatic energy; radiation; temperature extremes; engulfment; noise; and inwardly converging surfaces. Physical hazard also includes chemicals that can cause death or serious physical damage through skin or eye contact (rather than through inhalation).

Prohibited condition.  Any condition in a permit-required confined space that is not allowed by the permit during the authorized entry period.  For example: A hazardous atmosphere is a prohibited condition unless the employer can demonstrate that personal protective equipment (PPE) will provide effective protection for each employee in the permit space and provides the appropriate PPE to each employee.

Qualified person.  One who, by possession of a recognized degree, certificate, or professional standing, or who by extensive knowledge, training, and experience, has successfully demonstrated his ability to solve or resolve problems relating to the subject matter, the work, or the project.

Representative permit space.   A mock-up of a confined space that has entrance openings that are similar to, and is of similar size, configuration, and accessibility to, the permit space that authorized entrants enter.

Rescue.   Retrieving, and providing medical assistance to, one or more employees in a permit space.

Rescue service.  The personnel designated to rescue employees from permit-required confined spaces.

Retrieval system.  The equipment used for nonentry rescue of persons from permit-required confined spaces including: a retrieval line, full-body harness,  wristlets or anklets if appropriate,  and a lifting device or anchor.

Serious physical damage.   An impairment or illness in which a body part is made functionally useless or is substantially reduced in efficiency. Such impairment or illness may be permanent or temporary and includes, but is not limited to, loss of consciousness, disorientation, or other immediate and substantial reduction in mental efficiency. Injuries involving such impairment would usually require treatment by a physician or other licensed health-care professional.

Tagout.  (1) Placement of a tagout device on a circuit or equipment that has been deenergized, in accordance with an established procedure, to indicate that the circuit or equipment being controlled may not be operated until the tagout device is removed; and (2) The employer ensures that (i) tagout provides equivalent protection to lockout, or (ii) that lockout is infeasible and the employer has relieved, disconnected, restrained and otherwise rendered safe stored (residual) energy.

Testing.  The process of identifying and evaluating the hazards that entrants may be exposed to in a permit-required confined space.  Testing includes specifying the tests that are to be performed in the permit-required confined space.

Note: Testing allows employers to devise and implement adequate controls to protect entrants during entry, and to determine if acceptable entry conditions are present.

Ventilate or ventilation.   Controlling a hazardous atmosphere using continuous forced-air mechanical systems.

[Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  15-24-102 (Order 14-18), § 296-809-099, filed 12/01/2015, effective 01/05/2016.  Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  14-07-086 (Order 13-08), § 296-809-800, filed 03/18/14, effective 05/01/14.  Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  07-05-062, 07-06-005 (Order 06-38), § 296-809-800, filed 02/20/07, effective 04/01/07.  Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  04-03-081 (Order 02-15), § 296-809-800, filed 01/20/04, effective 05/01/04]

WAC 296-809-100 Scope.

This chapter applies to all confined spaces and provides requirements to protect employees from the hazards of entering and working in confined spaces.  This chapter applies in any of the following circumstances:

(1) You have confined spaces in your workplace.

Your employees will enter another employer's confined spaces.

A contractor will enter your confined spaces.

You provide confined space rescue services.

You can use Table 1 to help you decide which requirements to follow for confined spaces.

| Table 1 Requirements for Confined Spaces |
| --- |
| For confined spaces that are | The requirements in the following sections apply |
|  | 200 | 300 | 400 | 500 | 600 | 700 |
|  | Permit-required confined spaces | X | X | X | X | X | X |
|  | Permit-required confined spaces made safe through hazard elimination and reclassification to a non-permit confined space. | X | X | X | X | X | X |
|  | Permit required confined spaces entered by a contractor (or other outside employer). | X | X | X | X | X | X |
|  | Non-permit confined spaces Once the confined space meets the definition. | X |  |  |  |  | X |
|  | Never entered | X |  |  |  |  |  |
| If you only: |  |  |  |  |  |  |
|  | Use alternate entry procedures | X | X | X |  | X |  |
|  | Have a contractor (or outside employer) enter your space | X |  |  |  |  |  |
|  | Are a rescue service provider |  | X | X | X |  |  |
|  | Have non-permit confined spaces and your employees do not enter another employers permit-required confined spaces. | X |  |  |  |  | X |

Note: Requirements in other chapters may apply to your work. You can find a list of these rules in the resources section of this chapter. You will find some safety and health requirements are addressed on a broad level in this chapter, while being addressed for a specific application in another rule. When this happens, both requirements apply and should not conflict. When a conflict does occur, you need to follow the more specific requirement. If you are uncertain which requirements to follow, contact your local labor and industries (L&I) office. For a complete list of local L&I offices, see the resources section of the safety and health core rules, chapter 296-800 WAC.

Note. An employer cannot avoid the worker protection obligations of this standard by refusing to make decisions. For example, allowing employees to work in the proximity of or enter a PRCS without the required protections.

[Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  15-24-102 (Order 14-18), § 296-809-100, filed 12/01/2015, effective 01/05/2016.  Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  04-03-081 (Order 02-15), § 296-809-100, filed 01/20/04, effective 05/01/04].

WAC 296-809-200  Identifying and controlling permit-required confined spaces.

Summary

Your responsibility:  To identify your permit-required confined spaces and control employee entry.

| You must meet the requirements… | in this section: |
| --- | --- |
| Identify permit-required confined spaces | WAC 296-809-20002 |
| Inform employees and control entry to permit-required confined spaces | WAC 296-809-20004 |
| Follow these requirements when you contract with another employer to enter your confined space | WAC 296-809-20006 |

[Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  15-24-102 (Order 14-18), § 296-809-200, filed 12/01/2015, effective 01/05/2016.  Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  04-03-081 (Order 02-15), § 296-809-200, filed 01/20/04, effective 05/01/04].

WAC 296-809-20002  Identify permit-required confined spaces.

Identify all PRCS in your workplace.  Use the definitions of confined space and permit-required confined space found in the definition section of this chapter.  Consider each of the elements of the space.

Note: (a) If you enter the space prior to appropriately completing the reclassification process (for example to evaluate the hazard), you must follow the requirements in sections 300, 400, and 500 of this rule. (b) If you enter the space for any reason e.g. to determine the hazards by monitoring or testing, you must complete the requirements in sections 300 and 400 prior to entry and follow implementation requirements in section 500 Permit Entry Procedures during this entry.

.

Important: Process of identification of a permit-required confined space

Two step process to identifying permit required confined spaces: Identify each confined space based upon consideration and evaluation of each element of the confined space definition. See Appendix A of this chapter for Examples of Confined Spaces. Identify permit required confined space by evaluating the actual and potential hazards of each confined space based upon the definition of permit required confined space. See Appendix B of this chapter for Examples of Permit Required Confined Space Hazards.

Note: Proper application of the diagram/illustration in Appendix XX by a qualified and trained permit required confined space supervisor or competent person would facilitate compliance of this section.

[Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  15-24-102 (Order 14-18), § 296-809-20002, filed 12/01/2015, effective 01/05/2016.  Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  04-03-081 (Order 02-15), § 296-809-20002, filed 01/20/04, effective 05/01/04].

WAC 296-809-20004  Inform employees and control entry to permit-required confined spaces.

- You must provide information about confined spaces as follows:

(a) Make available to affected employees and their authorized representatives all information and documents required by this chapter.

  - Inform affected employees about the existence, location, and danger of any permit-required confined spaces in your workplace by:

(i)	Posting danger signs; or

(ii)	Using any other equally effective means to inform employees.1

(2)You must take effective measures to prevent unauthorized employees from entering permit-required confined spaces.2

1 Note: A sign reading “Danger-Permit Required Confined Space, do not enter” or using pictures or other similar wording employees can understand would satisfy the requirement for a sign.

2 Note: Examples of measures to prevent employee entry include: Padlocks Bolted covers. Use of special tools to remove covers along with employee training Permanently closing the space, such as welding it closed.

[Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  15-24-102 (Order 14-18), § 296-809-20004, filed 12/01/2015, effective 01/05/2016.  Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  04-03-081 (Order 02-15), § 296-809-20004, filed 01/20/04, effective 05/01/04].

WAC 296-809-20006  Follow these requirements when you contract with another employer to enter your confined space.

Important:

The contractor is responsible for following all confined space requirements in this chapter and in other rules that apply. For a list of other rules that may apply, see the resources section of this chapter.

You must do all of the following if you arrange to have another employer (contractor) perform work that involves entry into your permit-required confined space:

- Inform the contractor:

  - That the workplace contains permit-required confined spaces and entry is allowed only if the applicable requirements of this chapter are met.

  - Of the identified hazards and your experience with each permit-required confined space.

  - Of any precautions or procedures you require for the protection of employees in or near spaces where the contractor will be working  like timely notification of permit required confined spaces they identify.

- Coordinate entry operations with the contractor, when either employees or employers from the different companies will be working in or near permit-required confined spaces.

Discuss entry operations with the contractor when they are complete.  Include the following in your discussion:

  - The program followed during confined space entry; and

  - Any hazards confronted or created.

[Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  15-24-102 (Order 14-18), § 296-809-20006, filed 12/01/2015, effective 01/05/2016.  Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  04-03-081 (Order 02-15), § 296-809-20006, filed 01/20/04, effective 05/01/04].

WAC 296-809-300  Permit-required confined space program.

Summary

Your responsibility:  To develop your permit-required confined space program and practices.

| Before your employees enter you must meet these requirements… | in this section: |
| --- | --- |
| Develop a written permit-required confined space program | WAC 296-809-30002 |
| Meet these additional requirements if your employees enter another employer’s confined space | WAC 296-809-30004 |

Note. An employer cannot avoid the worker protection obligations of this standard by refusing to make decisions.  For example, allowing employees to work in the proximity of or enter a PRCS without the required protections.

[Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  15-24-102 (Order 14-18), § 296-809-300, filed 12/01/2015, effective 01/05/2016.  Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  04-03-081 (Order 02-15), § 296-809-300, filed 01/20/04, effective 05/01/04].

WAC 296-809-30002  Develop a written permit-required confined space program.

Important:

Identify and evaluate the hazards of permit-required confined spaces and the work performed, to assist you in developing your entry program and entry procedures.

- You must develop a written program, before employees enter, that describes the means, procedures, and practices you use for the safe entry of permit-required confined spaces as required by this chapter.  Include the following when applicable to your confined space entry program:

Documentation of permit entry procedures1.

Designation of employee roles (by name), such as entrants, attendants, entry supervisors, rescuers, or those who test or monitor the atmosphere in a permit-required space.

  - Identification of designated employee duties.

Training employees on their designated roles.

  - How to identify and evaluate hazards.

Use and maintenance of equipment.

How to prevent unauthorized entry.

How to coordinate entry with another employer.

How to rescue entrants.

- When applicable also include:

  - Documentation used for alternate entry procedures.

  - How to reclassify permit-required confined spaces to non-permit spaces.

Note: 1Examples of procedures: hazard identification, monitoring, energy control (lockout), ventilation (purging, flushing, use of local exhaust),inerting, engulfment control, equipment use, equipment maintenance, coordinating with an outside employer, rescue, and hazard elimination procedures to prepare for reclassification. For alternate entry, your written program only needs to meet the requirements of WAC 296-809-400, Employee training, and WAC 296-809-600, Alternate entry procedures, of this chapter.

(3)  You must consult with affected employees and their authorized representatives when developing and implementing all aspects of your permit-required confined space program.

(4) You must make the written program available to employees and their authorized representatives.

(5) You must update your written program as necessary. For example: you have identified deficiencies.

.

[Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  15-24-102 (Order 14-18), § 296-809-30002, filed 12/01/2015, effective 01/05/2016.  Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  04-03-081 (Order 02-15), § 296-809-30002, filed 01/20/04, effective 05/01/04].

WAC 296-809-30004  Meet these additional requirements if your employees enter another employer's confined space.

- You must obtain any available information about permit-required confined space hazards and entry operations from the host employer.

- You must coordinate entry operations with any other employers whose employees will be working in or near the permit-required confined space.

- You must inform the host employer, either through a debriefing or during entry operations, about:

  - The entry program you will follow; and

  - Any hazards you confronted or created in the space during entry operations.

Note: For multi-employer worksites, inform the host employer and authorized employee’s representative in a timely manner about the existence, location and the danger posed by, each permit space identified..

[Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  15-24-102 (Order 14-18), § 296-809-30004, filed 12/01/2015, effective 01/05/2016.  Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  04-03-081 (Order 02-15), § 296-809-30004, filed 01/20/04, effective 05/01/04].

WAC 296-809-400  Employee Training.

Summary

Your responsibility:  To make sure employees are trained to perform their designated roles safely.

| You must meet these requirements prior to entry into permit required confined spaces… | in this section: |
| --- | --- |
| Provide employee training | WAC 296-809-40002 |
| Certify employee proficiency | WAC 296-809-40004 |

[Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  15-24-102 (Order 14-18), § 296-809-400, filed 12/01/2015, effective 01/05/2016.  Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  04-03-081 (Order 02-15), § 296-809-400, filed 01/20/04, effective 05/01/04].

WAC 296-809-40002  Provide employee training.See other document

- You must provide training to each employee involved in permit-required confined space activities, so they acquire the understanding, knowledge and skills necessary to safely perform assigned duties.

  - Establish employee proficiency in their confined space duties.

(b) Introduce new or revised procedures as necessary.

You must provide training at the following times:

  - Before an employee is first assigned to duties covered by this chapter.

(b) Before there is a change in an employee's assigned duties.

(c)When there is a permit-required confined space hazard for which the employee has not already been trained.

(d) If you have reason to believe that there are either:

(i)	Deviations from our procedures for permit-required confined space entry; or

(ii)	Employee knowledge or use of your procedure is inadequate.

Note: Training must result in understanding of the hazards of permit space(s), the methods used to isolate, control and protect workers from permit required confined space hazards. For those workers not authorized to perform entry rescue, training must include the dangers of attempting rescue. Training must both be in a language and vocabulary the worker can understand

[Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  15-24-102 (Order 14-18), § 296-809-40002, filed 12/01/2015, effective 01/05/2016.  Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  04-03-081 (Order 02-15), § 296-809-400, filed 01/20/04, effective 05/01/04].

WAC 296-809-40004  Certify employee proficiency.

- You must certify employee proficiency in their assigned duties.

- You must make sure the certification:

  - Contains each employee's name, the trainer's written or electronic signature or initials, and the dates of training.

(b) Is available for inspection by employees and their authorized representatives.

Note: Employers can determine employee proficiency by: Observing employee performance during training exercises that simulate actual confined space conditions. A comprehensive written examination; or Any other method that is effective for the employer.

[Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  15-24-102 (Order 14-18), § 296-809-40004, filed 12/01/2015, effective 01/05/2016.  Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  04-03-081 (Order 02-15), § 296-809-400, filed 01/20/04, effective 05/01/04].

WAC 296-809-500  Permit-entry procedures.

Summary

Your responsibility:  To establish procedures for the safe permit-required entry of confined spaces.

| You must meet the requirements… | in this section: |
| --- | --- |
| Implement procedures for safe entry into permit required confined space | WAC 296-809-50002 |
| Use an entry permit that contains all required information | WAC 296-809-50004 |
| Keep and review your entry permits | WAC 296-809-50006 |
| Prevent unauthorized entry | WAC 296-809-50008 |
| Provide, maintain and use proper equipment | WAC 296-809-50010 |
| Evaluate and control hazards for safe entry | WAC 296-809-50012 |
| Make sure you have adequate rescue and emergency service available | WAC 296-809-50014 |
| Use nonentry rescue systems or methods whenever possible | WAC 296-809-50016 |
| Make sure entry supervisors perform their responsibilities and duties | WAC 296-809-50018 |
| Provide an attendant outside the permit-required confined space | WAC 296-809-50020 |
| Make sure entrants know the hazardous conditions and their duties | WAC 296-809-50022 |
| Implement procedures for ending entry | WAC 296-809-50024 |

[Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  15-24-102 (Order 14-18), § 296-809-500, filed 12/01/2015, effective 01/05/2016.  Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  04-03-081 (Order 02-15), § 296-809-500, filed 01/20/04, effective 05/01/04].

WAC 296-809-50002  Implement procedures for entry permits.

- You must identify and evaluate, before employees enter, potential hazards from:

(a) The permit-required confined space; and

(b)  The work to be performed.

You must complete an entry permit before entry is authorized; documenting that you have completed the means, procedures, and practices, necessary for safe entry and work.

You must make sure that entrants or their representatives have an opportunity to observe any monitoring or testing, or any actions to eliminate or control hazards, performed to complete the permit.

You must identify the entry supervisor and make sure the entry supervisor signs the entry permit, authorizing entry, before the space is entered.

You must make the completed permit available to entrants or their authorized representatives at the time of entry.  Do this by either posting the completed permit at the entry location, or by any other equally effective means.

You must make sure the duration of the permit does not exceed the time required to complete the assigned task or job identified on the permit.

You must note any problems encountered during an entry operation on the permit.  Use the information to make appropriate revisions to your program, entry operations, means, systems, procedures and practices.

[Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  15-24-102 (Order 14-18), § 296-809-50002, filed 12/01/2015, effective 01/05/2016.  Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  04-03-081 (Order 02-15), § 296-809-400, filed 01/20/04, effective 05/01/04].

WAC 296-809-50004  Use an entry permit that contains all required information.

You must make sure your entry permit identifies all of the following that apply to your entry operation:

- The space to be entered.

- Purpose of the entry.

- Date and the authorized duration of the entry permit.

- Hazards of the space to be entered.

- Acceptable entry conditions.

- Results of initial and periodic tests performed to evaluate and identify the hazards and conditions of the space, accompanied by the names or initials of the testers and by an indication of when the tests were performed.

Appropriate measures used before entry to isolate the space, and eliminate or control hazards.  Examples of appropriate measures include the lockout or tagging of equipment and procedures for purging, inerting, ventilating, and flushing permit-required confined spaces.

Names of entrants and current attendants.  Other means include the use of rosters or tracking systems as long as the attendant can determine quickly and accurately, for the duration of the permit, which entrants are inside the space.

The current entry supervisor.

A space for the signature or initials of the original supervisor authorizing entry.

Communication procedures for entrants and attendants to maintain contact during the entry.

Equipment provided for safe entry, such as:

(a) Personal protective equipment (PPE).

(b) Testing equipment.

(c) Communications equipment.

(d) Alarm systems.

(e) Rescue equipment.

Rescue and emergency services available, and how to contact them.  Include equipment to use, and names and contact information.

Other information needed for safety in the particular confined space.

Additional permits issued for work in the space, such as for hot work.

[Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  15-24-102 (Order 14-18), § 296-809-50004, filed 12/01/2015, effective 01/05/2016.  Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  04-03-081 (Order 02-15), § 296-809-50004, filed 01/20/04, effective 05/01/04].

WAC 296-809-50006  Keep and review your entry permits.

- You must keep entry permits for at least one year.

You must keep entry permits or other atmospheric monitoring records that show the actual atmosphere an employee entered or worked in, as employee exposure records.

You must review your permit-required confined space entry program by conducting a review when you have any reason to believe your entry program may not protect employees, and revise your program before allowing subsequent entries.

Note: Examples of circumstances requiring the review of your program include the following: There is unauthorized entry of a permit space. A permit space hazard not covered by the permit is found. A condition prohibited by the permit occurs. An injury or near-miss occurs during entry. There is a change in the use or configuration of a permit space. An employee complains about the effectiveness of the program.

You must review canceled entry permits within one year following each entry to evaluate:

  - Your permit-required confined space program.

(b)  The protection provided to employees entering permit-required confined spaces.

You must update your written permit-required confined space entry program as necessary.

Note: Employers may perform a single annual review covering all entries performed during a 12-month period. If no entry is performed during a 12-month period, no review is necessary.

Reference: Keep employee exposure records according to chapter 296-802 Employee Medical and Exposure Records.

[Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  15-24-102 (Order 14-18), § 296-809-50006, filed 12/01/2015, effective 01/05/2016.  Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  04-03-081 (Order 02-15), § 296-809-50006, filed 01/20/04, effective 05/01/04].

WAC 296-809-50008  Prevent unauthorized entry.

You must implement measures necessary to prevent unauthorized entry into permit-required confined spaces, when conducting authorized entry.

Note: When removing entrance covers to open the confined space, protect entrants and those outside the confined space from hazards. Examples of measures to prevent unauthorized entry are signs, physical barricades, warning tape, and an attendant.

[Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  15-24-102 (Order 14-18), § 296-809-50008, filed 12/01/2015, effective 01/05/2016.  Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  04-03-081 (Order 02-15), § 296-809-50008, filed 01/20/04, effective 05/01/04].

WAC 296-809-50010  Provide, maintain, and use proper equipment.

- You must provide the equipment in Table 2, when needed and at no cost to employees.

- You must make sure that employees use provided equipment properly.

- You must maintain the provided equipment.

| Table 2 Equipment Provided to Employees at No Cost |
| --- |
| Type of equipment | For |
| Testing and monitoring equipment | Evaluating permit-required confined space conditions |
| Ventilating equipment | Obtaining and maintaining acceptable entry conditions |
| Communication equipment | Effective communication between the attendant and the entrants and to initiate rescue when required |
| Personal protective equipment (PPE) | Protecting employees from hazards of the space or the work performed |
| Lighting equipment | Employees to see well enough to work safely and to exit the space quickly in an emergency |
| Barriers or shields, such as pedestrian, vehicle or other barriers | Protecting employees from hazards outside of the space |
| Ladders | Safe entry and exit by entrants |
| Rescue and emergency equipment, except for equipment provided by the rescue service provider | Safe and effective rescue |
| Any other equipment | Safe entry into and rescue from permit-required confined spaces |

[Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  15-24-102 (Order 14-18), § 296-809-50010, filed 12/01/2015, effective 01/05/2016.  Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  04-03-081 (Order 02-15), § 296-809-50010, filed 01/20/04, effective 05/01/04].

WAC 296-809-50012  Evaluate and control hazards for safe entry.

- You must evaluate and control hazards for safe entry into permit-required confined spaces by doing all the following:

(a) Test for atmospheric hazards, in this order:

(i)	Oxygen

(ii)	Combustible gases and vapors.

(iii) Toxic gases and vapors.

(b) Provide each entrant or their authorized representative an opportunity to observe any of the following:

(i)	Preentry testing.

(ii)	Subsequent testing.

(iii) Monitoring of permit-required spaces.(c) Reevaluate the permit-required space in the presence of any entrant, or their authorized representative, who requests this to be done because they have reason to believe that the evaluation of that space may not have been adequate.

(d) Upon request, immediately provide each entrant or their authorized representative, with the results of any testing required by this rule.

(e) Continuously monitor conditions in areas where entrants are working, when isolation of the space is not feasible.

Examples would be a large space or space that is part of a continuous system, such as a sewer.

You must evaluate space conditions during entry as follows:

| Table 3 Evaluating Space Conditions |
| --- |
| You must: | In order to: |
| Test conditions before entry | Determine that acceptable entry conditions exist before entry is authorized by the entry supervisor |
| Test or evaluate space conditions during entry | Determine that acceptable entry conditions are being maintained during entry operations |
| Evaluate entry operations | Make sure entrants of more than 1 employer working at the same time in or around a permit-required confined space, do not endanger each other |

Important: This section applies to both:

Employers whose employees use permit entry procedures; and Employers who provide rescue services.

[Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  15-24-102 (Order 14-18), § 296-809-50012, filed 12/01/2015, effective 01/05/2016.  Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  04-03-081 (Order 02-15), § 296-809-50012, filed 01/20/04, effective 05/01/04].

WAC 296-809-50014  Make sure you have adequate rescue and emergency services available.

- You must make sure you have adequate rescue and emergency services available during your permit-required confined space entry operations.

(a) Evaluate and select rescue teams or services who can:

(i)	Respond to a rescue call in a timely manner.  Timeliness is based on the identified hazards.  Rescuers must have the capability to reach potential victims within an appropriate time frame based on the identified permit space hazards.

(ii)	Proficiently rescue employees from a permit-required confined space in your workplace.  Rescuers must have the appropriate equipment for the type of rescue.

(b) Make sure that at least one member of the rescue team or service holds a current certification in first aid and cardiopulmonary resuscitation (CPR).

(c)Inform each rescue team or service about the hazards they may confront when called to perform rescue.

(d) Provide the rescue team or service with access to all permit spaces from which rescue may be necessary.  This will allow them to develop appropriate rescue plans and to practice rescue operations.

Note: What will be considered timely will vary according to the specific hazards involved in each entry. For example, chapter 296-842 WAC, Respirators, requires that employers provide a standby person or persons capable of immediate action to rescue employee(s) for work areas considered to contain an IDLH atmosphere. If the rescue service becomes unavailable during the course of an entry, the rescue service must contact the permit required confined space supervisor in a timely manner to cancel the permit-required confined space entry.

You must provide employees assigned to provide permit-required confined space rescue and emergency services must be provided, at no cost to the employee, with:

  - Personal protective equipment (PPE) needed for safe entry.

  - Other equipment required to conduct rescues safely.

(c)  Training so they are:

(i)	Proficient in the use of the PPE and other equipment.

(ii)	Proficient in an entrant of permit-required confined spaces.

(iii)	Able to safely perform assigned rescue and emergency duties.

(iv) Knowledgeable in basic first aid and cardiopulmonary resuscitation (CPR).

(d) Practice sessions for permit-required confined space rescues at least once every 12 months where dummies, manikins, or actual persons are removed from either:

(i)	The actual permit spaces; or

(ii)	Representative permit spaces that simulate the opening size, configuration, and accessibility, of permit spaces where rescue will be performed.

You must establish procedures for:

  - Contacting rescue and emergency services.

  - Rescuing entrants from permit-required confined spaces.

  - Providing necessary emergency services to rescued entrants.

  - Preventing unauthorized persons from attempting a rescue.

[Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  15-24-102 (Order 14-18), § 296-809-50014, filed 12/01/2015, effective 01/05/2016.  Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  09-05-071 (Order 08-35), § 296-809-50014, filed 02/17/09, effective 04/01/09].  Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  04-03-081 (Order 02-15), § 296-809-50014, filed 01/20/04, effective 05/01/04].

WAC 296-809-50016  Use nonentry rescue systems or methods whenever possible.

- You must use nonentry retrieval systems or methods to rescue entrants in a permit-required confined space unless this:

  - Would increase the overall risk of injury to entrants; or

(b)  Would not contribute to the rescue of the entrant.

(2)You must make sure each entrant uses a chest or full-body harness, with a retrieval line attached to the harness at one of the following locations:

(a) At the center of the employee's back, near shoulder level.

(b) Above the employee's head.

(c) At another point which presents a profile small enough for the successful removal of the employee.(3)  You must attach the retrieval line to a mechanical device or fixed point outside the space, so rescue can begin as soon as necessary.

(4)  You must make sure a mechanical device is available to retrieve entrants from vertical spaces more than 5 feet (1.52 m) deep.

Note: When you can demonstrate that the use of a chest or full-body harness is not feasible or creates a greater hazard, then you may use wristlets or another method shown to be the safest and most effective alternative.

[Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  15-24-102 (Order 14-18), § 296-809-50016, filed 12/01/2015, effective 01/05/2016.  Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  04-03-081 (Order 02-15), § 296-809-50016, filed 01/20/04, effective 05/01/04].

WAC 296-809-50018  Make sure entry supervisors perform their responsibilities and duties.

You must make sure that an entry supervisor:

- Authorizes the entry into a permit-required confined space by signing the entry permit.

- Oversees entry operations.

- Knows about the hazards that may be faced during entry, including the mode, signs or symptoms, and consequences of the exposure.

- Verifies and checks all of the following:

  - The appropriate entries have been made on the permit.

(b)All tests specified by the permit have been conducted.

(c) All procedures and equipment specified by the permit are in place before approving the permit and allowing entry to the space.

Terminates the entry and cancels the permit when:

  - The assigned task or job has been completed.

  - A condition in the space that is not covered by the entry permit is discovered.

Verifies that rescue services are available; the means to contact them is operable; and the employer will be notified as soon as the service becomes unavailable..

Removes unauthorized individuals who enter or attempt to enter the permit-required confined space during entry operations.

Determines that entry operations remain consistent with the terms of the entry permit and acceptable entry conditions are maintained:

  - Whenever responsibility for a permit-required space entry operation is transferred; and

  - At regular intervals dictated by the hazards and operations performed within the space.

Note: Make sure entry supervisors have the required knowledge and proficiency to perform the job duties and responsibilities required by this chapter. The entry supervisor may also perform other duties under this chapter, such as attendant or entrant, if they are trained and proficient in those duties. The responsibility of the entry supervisor may be passed from one supervisor to another during an entry operation.

[Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  15-24-102 (Order 14-18), § 296-809-50018, filed 12/01/2015, effective 01/05/2016.  Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  04-03-081 (Order 02-15), § 296-809-50018, filed 01/20/04, effective 05/01/04].

WAC 296-809-50020  Provide an attendant outside the permit-required confined space.

Important:

The number of attendants assigned should be tailored to the requirements of the space and the work performed. You need to assess if it is appropriate or possible to have multiple permit spaces monitored by a single attendant, or have an attendant stationed at a location outside each space. Video cameras and radios are examples of tools that may assist an attendant monitoring more than one space. Attendants may be stationed at any location outside the permit-required confined space if the duties described in this section can be effectively performed for each space that is monitored.

- You must provide at least one attendant that must remain outside the permit-required confined space during entry operations.

- You must make sure each permit-required confined space attendant:

  - Understands the hazards that may be faced during entry, including the mode, signs or symptoms, and results of exposure to the hazards.

  - Is aware of the behavioral effects of exposure to the hazard.

  - Continuously maintains an accurate count of entrants in the space.

  - Maintains an accurate record of who is in the permit-required confined space.

  - Communicates with entrants as necessary to monitor their status or alert them of the need to evacuate the space.

(f) Monitors activities inside and outside the space to determine if it is safe for entrants to remain in the space.

(g) Orders entrants to evacuate the space immediately if any of the following conditions occur:

(i)	A prohibited condition.

(ii)	The behavioral effects of hazardous exposure in an entrant.

(iii)A situation outside the space that could endanger entrants.

(iv)	The attendant cannot effectively and safely perform all the duties required in this chapter.

(h) Takes the following actions when unauthorized persons approach or enter a space:

(i)	Warns unauthorized persons to stay away from the space.

(ii)	Tells the unauthorized persons to exit immediately if they have entered the space.

(iii)  Informs entrants and the entry supervisor if unauthorized persons have entered the space.

(i)Performs nonentry rescues as specified by our rescue procedure.

(j)  Has the means to respond to an emergency affecting one or more of the permit spaces being monitored without preventing performance of the attendant’s duties to the other spaces being monitored.

(k) Carries out no duties that might interfere with their primary duty to monitor and protect the entrants.

(l) Calls for rescue and other emergency services as soon as entrants may need assistance to escape from the space.

(m) Monitors entry operations until relieved by another attendant or all entrants are out of the space.

[Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  15-24-102 (Order 14-18), § 296-809-50020, filed 12/01/2015, effective 01/05/2016.  Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  04-03-081 (Order 02-15), § 296-809-50020, filed 01/20/04, effective 05/01/04].

WAC 296-809-50022  Make sure entrants know the hazardous conditions and their duties.

You must make sure that all entrants:

- Know the hazards they may face during entry, including the mode, signs or symptoms, and results of exposure to the hazards.

- Use equipment properly.

- Communicate with the attendant as necessary so the attendant can:

Monitor entrant status, and

Alert entrants of the need to evacuate.

Alert the attendant whenever either of these situations exist:

A warning sign or symptom of exposure to a dangerous situation such as, behavioral changes, euphoria, giddiness potentially from lack of oxygen or exposure to solvents.

A prohibited condition.

Exit from the permit-required confined space as quickly as possible when one of the following occurs:

The attendant or entry supervisor gives an order to evacuate.

The entrant recognizes any warning sign or symptom of exposure to a dangerous situation.

The entrant detects a prohibited condition.

An evacuation alarm is activated.

[Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  15-24-102 (Order 14-18), § 296-809-50022, filed 12/01/2015, effective 01/05/2016.  Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  04-03-081 (Order 02-15), § 296-809-50022, filed 01/20/04, effective 05/01/04].

WAC 296-809-50024  Implement procedures for ending entry.

You must make sure you terminate the entry when entry operations are completed, including securing an entrance cover and canceling the permit.

[Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  15-24-102 (Order 14-18), § 296-809-50024, filed 12/01/2015, effective 01/05/2016.  Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  04-03-081 (Order 02-15), § 296-809-50024, filed 01/20/04, effective 05/01/04].

WAC 296-809-600  Alternate entry procedures.

Summary

Your responsibility:  To choose alternate entry procedures for spaces where the only hazard is a hazardous atmosphere.

Important: In addition to this section, you also need to meet the requirements in the following sections of this chapter:

WAC 296-809-200, Identifying and controlling permit-required confined spaces. WAC 296-809-300, Permit-required confined space program. WAC 296-809-400, Employee training.

| You must meet the requirements… | in this section: |
| --- | --- |
| Make sure the following conditions are met if using alternate entry procedures | WAC 296-809-60002 |
| Follow these alternate entry procedures for permit-required confined spaces | WAC 296-809-60004 |

[Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  15-24-102 (Order 14-18), § 296-809-600, filed 12/01/2015, effective 01/05/2016.  Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  04-03-081 (Order 02-15), § 296-809-600, filed 01/20/04, effective 05/01/04].

WAC 296-809-60002  Make sure the following conditions are met if using alternate entry procedures.

- You must make sure, when using alternate entry procedures, instead of permit entry procedures, that you have monitoring and inspection data that supports the following:

That the only hazard of the permit-required confined space is an actual or potentially hazardous atmosphere.

That continuous forced air ventilation alone is all that is needed to maintain the permit-required confined space for safe entry.

(2)	You must make sure an entry to obtain monitoring and inspection data or to eliminate hazards is performed according to WAC 296-809-500, Permit entry procedures.

- You must make sure all documentation produced is available to each affected employee and their authorized representative.

[Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  15-24-102 (Order 14-18), § 296-809-60002, filed 12/01/2015, effective 01/05/2016.  Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  04-03-081 (Order 02-15), § 296-809-60002, filed 01/20/04, effective 05/01/04].

WAC 296-809-60004  Follow these alternate entry procedures for permit-required confined spaces.

You must use the following alternate entry procedures:

- Eliminate any unsafe conditions before removing an entrance cover.

When entrance covers are removed, promptly guard the opening with a railing, temporary cover, or other temporary barrier to prevent accidental falls through the opening and protect entrants from objects falling into the space.

Certify that preentry measures have been taken (such as safe removal of the cover and having protection needed to gather preentry data), with the date, location of the space, and signature of the person certifying.

Make the preentry certification available before entry to each entrant.

Before an employee enters the confined space, test the internal atmosphere with a calibrated, direct-reading instrument for all of the following, in this order:

Oxygen content.

Flammable gases and vapors.

Potential toxic air contaminants.

Provide entrants, or their authorized representatives, with an opportunity to observe the preentry and periodic testing.

Make sure the atmosphere within the space is not hazardous when entrants are present.

Use continuous forced air ventilation, as follows:

Wait until the forced air ventilation has removed any hazardous atmosphere before allowing entrants into the space.

Direct forced air ventilation toward the immediate areas where employees are, or will be, and continue ventilation until all employees have left the space.

Provide the air supply from a clean source and make sure it does not increase hazards in the space.

Test the atmosphere within the space as needed to make sure hazards do not accumulate.

If a hazardous atmosphere is detected during entry, do all of the following:

Evacuate employees from the space immediately.

Evaluate the space to determine how the hazardous atmosphere developed.

Implement measures to protect employees from the hazardous atmosphere before continuing the entry operation.

Verify the space is safe for entry before continuing the entry operation.

[Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  15-24-102 (Order 14-18), § 296-809-60004, filed 12/01/2015, effective 01/05/2016.  Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  04-03-081 (Order 02-15), § 296-809-60004, filed 01/20/04, effective 05/01/04].

WAC 296-809-700  Nonpermit confined spaces requirements.

Summary

Your responsibility:  To make sure any space you classify as nonpermit, does not have the potential to contain serious health or safety hazards.

| You must meet the requirements… | in this section: |
| --- | --- |
| Follow these requirements when classifying a confined space as a nonpermit confined space | WAC 296-809-70002 |
| Reevaluate nonpermit confined spaces if hazards develop. | WAC 296-809-70004 |

Important:

A confined space may be classified as a nonpermit confined space for as long as the hazards remain eliminated. Once a hazard is present, you must follow all requirements of this chapter that apply. Confined space hazards may evolve over time. Work in a confined space may also introduce hazards not native to the space. For example: hazards may develop during entry due to changing conditions in the space, and some hazards generated exterior to the space may directly affect an entrant or attendant. like atmospheric hazards like vehicle exhaust from vehicles idling outside the space .. TO reclassify a permit required confined space, you must evaluate the confined space for potential and actual hazards. For spaces meeting the criteria, you may reclassify it as nonpermit confined space by 1) eliminating the hazards and 2) completing the documentation required by WAC 296-809-700. Spaces not meet the criteria of the section at any time before, during or after entry remain classified as Permit Required Confined Space.

[Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  15-24-102 (Order 14-18), § 296-809-700, filed 12/01/2015, effective 01/05/2016.  Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  04-03-081 (Order 02-15), § 296-809-700, filed 01/20/04, effective 05/01/04].

WAC 296-809-70002  Follow these requirements when classifying a confined space as a nonpermit confined space.

- You must make sure the confined space meets these conditions to be classified as nonpermit confined spaces:

The confined space does not contain an actual or potential hazardous atmosphere.

The confined space does not contain hazards capable of causing death or serious physical harm.  This includes any recognized health or safety hazards including engulfment in solid or liquid material, electrical shock, or moving parts.

If you must enter to remove hazards, the space must be treated as a permit-required confined space until hazards have been eliminated.

Note: Controlling atmospheric hazards through forced air ventilation does not eliminate the hazards. You should evaluate the use of lockout-tagout, as covered in chapter 296-803 WAC, to determine if using it fully eliminates the hazard. You are allowed to use alternate entry procedures covered in WAC 296-809-600, if you can demonstrate that forced air ventilation alone will control all hazards in the space.

You must document how you determined the confined space contained no permit-required confined space hazards.  Certify this documentation with the following:

  - Date.

(b) Location of the space.

(c)  Signature of the person making the determination.

You must make the certification available to each entrant, or their authorized representative.

Note: This certification must be completed every time a permit-required confined space is reclassified as a nonpermit space.

[Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  15-24-102 (Order 14-18), § 296-809-70002, filed 12/01/2015, effective 01/05/2016.  Statutory Authority:  Statutory Authority:  RCW 49.17.010, .020, .040, .050, and .060.  07-03-163 (Order 06-30), § 296-809-70002, filed 01/24/07, effective 04/01/07.  Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  04-03-081 (Order 02-15), § 296-809-70002, filed 01/20/04, effective 05/01/04].

WAC 296-809-70004  Reevaluate nonpermit confined spaces if hazards develop.

- You must reclassify a nonpermit confined space to a permit-required confined space, if necessary, when changes in the use or configuration of the space increase the hazards to entrants.

- You must make sure all employees exit the space if hazards develop.  You must then reevaluate the space and determine whether it must be reclassified as a permit-required confined space.

[Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  15-24-102 (Order 14-18), § 296-809-70004, filed 12/01/2015, effective 01/05/2016.  Statutory Authority:  Statutory Authority:  RCW 49.17.010, .040, .050, and .060.  04-03-081 (Order 02-15), § 296-809-70004, filed 01/20/04, effective 05/01/04].